## Slide 1
SHADOW4: the popular ray tracing revived for evolving synchrotron sources in 4th-generation storage rings
Manuel Sánchez del Río*1, Juan Reyes-Herrera1, Xianbo Shi2 and Luca Rebuffi2
*srio@esrf.eu
1Advanced Analysis & Precision Unit, MEG/ISDD, ESRF
2APS-Argonne National Lab
Mikrosymposium MS 1/1: Beamline Optics and Diagnostics: 13:00 Tuesday 27 August, 2024

## Slide 2: 40 YEARS OF Shadow
Franco Cerrina (♰2010)
SHADOW
M. Sanchez del Rio, et al.J. Synchr. Rad.18, (2011) http://dx.doi.org/10.1107/S0909049511026306
Python API
XOP/ShadowVUI
Kernel (Fortran9x)
Generic ray tracing package for optics
Specialized in SR (storage ring sources, grazing optics, crystals…)
Helped to most 2-4th generations of SR facilities
Used/cited in a huge number of papers
SHADOW 1 & 2
SHADOW3
SHADOW1 1984-1990 VAX-VMS mainframes
SHADOW2 1990-2010 Unix workstations+Windows

## Slide 3: 2014: ShadowOUI1= SHADOW3 + ORANGE2
SIZE RESOLUTION FLUX
0.6 eV
---> Integrated Flux : 1.25321e+13 ph/s
[1] L Rebuffi and M Sanchez del Rio J Synchr. Rad. 23 1357-1367 (2016) https://doi.org/10.1107/S1600577516013837
[2] https://orangedatamining.com/

## Slide 4: ShadowOUI: not only SHADOW3
Corrections for coherent optics (HYBRID1)
Surface error databases DABAM, DABAM2D (see poster R. Celestre 1.181)
Preprocessors (surfaces, reflectivity, VLS, diaboloids2)
Elements: CRL, TF, Benders, etc.
Loops & Heat load loops3
New crystal structures (high d-spacing4)
[1] Shi et al. 2014 https://doi.org/10.1107/S160057751400650X
[2] Sanchez del Rio et al. 2021 https://doi.org/10.1107/S160057752100401X
[3] Rebuffi et al. 2020 https://doi.org/10.1107/S160057752000778X
[4] Yu et al. 2022 https://doi.org/10.1107/S160057752200707X

## Slide 5: OASYS add-ons
SRW
XOPPY
SYNED
Facility Add-Ons, e.g. ESRF
WOFRY
SHADOWOUI
WISER
OASYS Main
SHADOW4
XRayServer, …
Tools
Ray tracing
Wave optics
1.3
INTEROPERABILITY
https://oasys-kit.github.io
Extensions
Notes: Before starting, I would like to do the following statement, all calculations presented here were performed using OASYS tools

## Slide 6: SHADOW4
SHADOW4 is a new Kernel, and a new interface, for new generations of sources
Fully developed in Python
OO programming
OASYS experience and ad-hoc developments
Fast enough
Preparing 5th generation
SHADOW is an interactive tool adapted for common laptops
Just called SHADOW4
Simplified interface (less widgets, generic mirrors, crystals, etc.)
Optimized (better communication)
Automatic scripting
Facilitate interoperability with other tools (e.g. for partial coherence)
Adapted for AI integration and Digital Twins (see L Rebuffi’s talk 3/3 Fri 14:00)
Easy transition from laptop prototyping to High-Performance Computing (HPC) and Cloud Computing
Open Source and Collaborative Development
Educational material for interactive leaning
Fortran: compilation: obsolete technology, poorly structured code
Python API maintenance and extension
Python packaging (wheels)
SHADOW3 problems:

## Slide 7: Shadow4 Kernel: Application User Interface
S4Beam: traditional beam data (nrays, 18)
Automated scripts with OASYS
Documentation: https://shadow4.readthedocs.io
API
S4Beamline
S4LightSource
S4BeamlineElement
S4ElectronBeam
S4MagneticStructure
S4OpticalElement
ElementCoordinates
…

## Slide 8: Shadow4 Kernel: beamline components
[1] https://arxiv.org/abs/2406.16446
Optical elements
  S4Screen (screens, slits, stops, absorbers)
  S4IdealLens, S4Empty,… (ideal elements)
  S4PlaneMirror, S4SphereMirror, S4EllipsoidalMirror, …, S4AdditionalNumericalMeshMirror
  S4PlaneGrating, … (including VLS)
  S4PlaneCrystal, … (undistorted perfect crystals in reflection)
  S4PlaneMultilayer, … (also graded, in depth or laterally)
  S4Interface, S4Lens, S4CRL, S4Transfocator (refractors)
Sources/Magnetic structures
  SourceGeometrical, SourceGridCartesian, SourceGridPolar)
  S4BendingMagnet (upgraded methods1)
  S4Wiggler (included short IDs)
  S4GaussianUndulator, S4Undulator (upgraded: see talk 1/2 of Juan Reyes-Herrera Today 18:15)

## Slide 9: Shadow4 Kernel: models and algorithms
  S4OpticalSurface (S4Conic1, S4Toroid, S4Mesh)
  Include methods for reflection, refraction, grating scattering
[1] https://arxiv.org/abs/2406.04079
[2] https://arxiv.org/abs/2406.16960 https://github.com/oasys-kit/crystalpy
[3] https://github.com/tschoonj/xraylib
[4] https://github.com/oasys-kit/dabax
Optical constants (scattering factors, refraction indices, crystal structures)
  preprocesor data file
  direct link
    xraylib3
    DABAX4
  PreRefl: Absorption/refraction for attenuators, mirrors, lenses
  crystalpy2: external library for Crystals
  MLayer
Physical model (reflectivities)
preprocessors
code
Geometrical model

## Slide 10: Shadow4: advanced tools – Hybrid1 method
Corrects ray tracing considering scattering and diffraction when the beam has a high coherence
Includes scattering by o.e.’s boundaries (slits, mirrors, gratings, lenses)
Manages the surface error (delegated from o.e.)
Fully rewritten code2
Scriptable
[1] Shi et al. 2014 https://doi.org/10.1107/S160057751400650X
[2] https://github.com/oasys-kit/shadow4-advanced

## Slide 11: Shadow4: beta testers are welcomed!
Send issues in https://github.com/oasys-kit/shadow4/issues
Shadow3
Shadow4
beam converter
matching results

## Slide 12: Shadow4: summary
SHADOW4 is announced
  New Kernel fully in python, modern OO programming
  New interface in OASYS, including Hybrid
  Preparing the future SR generations
Already available in OASYS [beta]
Didactical material1,2 available.
Future OASYS schools (done at ESRF3,4, APS3, ALS5)
[1] https://github.com/oasys-esrf-kit/oasys_hercules_2024
[2] https://github.com/oasys-kit/shadow4workspaces
[3] https://github.com/oasys-kit/oasys_school
[4] https://doi.org/10.1080/08940886.2019.1654832
[5] https://doi.org/10.1080/08940886.2023.2274746

## Slide 13
Thank you
Download slides:

## Slide 14: HIerarchical1 BEAMLINE simulations with Oasys
Analytical model (by hand)
Ray tracing (Shadow4)
Hybrid model (Shadow4)
wave optics & partial coherence 1D (WOFRY) (see poster 1.141)
wave optics partial coherence 2D:
Monte Carlo (multi e-) (SRW)
Coherent Mode Decomposition (COMSYL)
[1] M. Sanchez del Rio et al. 2019 https://doi.org/10.1107/S160057751901213X
COMPLEXITY
Page 14